## Slide 1: very A ^ short introduction to the Battery Programming Box Boot Camp 2022

## Slide 2
Device Overview
Small device used to access battery ICs
  Reads/Writes EEPROM, Auth IC, and Gas Gauge
USB interface, appears as a serial port and 2MB Flash drive
    Simple command line interface
    Drag & drop files to/from the drive
Supports most Zebra terminal battery types
Status LED for connection/battery status
Terminal strip for battery socket connections
Device parts cost is ~$50 each
Zebra Confidential: For Internal Use Only

## Slide 3
Zebra Confidential: For Internal Use Only
Batteries Supported
MPA2 Smart Batteries (MC33 legacy)
Pollux batts (TC70)
PP+ Batts (TC70X, TC51, TC8000, MC18, etc.)
Value tier (TC21, MC22, etc.)
PP+ V2 (New GG) (Jaws, etc.)
Hardware support for BLE battery
  Simulate terminal power modes (on, off, suspended)
  Simulate battery in & out of terminal
Hardware can support Zebra printer 2 cell packs

## Slide 4
Zebra Confidential: For Internal Use Only
Capabilities
Read\write EEPROM/Auth IC hex file data to/from internal 2MB drive
Validate battery data to check for errors
Authenticate the Auth IC
Display battery voltage and thermistor resistance
Display battery EEPROM/Auth IC data in human readable form
  Part number, revision, JEITA data, etc.
Display gas gauge data in human readable form
  Cycle count, accumulated charge, time since first use, status registers, etc.
Update/replace EEPROM/Auth IC hex data
Update Gas Gauge data & firmware

## Slide 5
Zebra Confidential: For Internal Use Only
Uses
Engineering/Testing
  Creating batteries with know errors to check terminal/toaster firmware
  Updating battery/gas gauge data
    Jaws “0%” batts that had bad GG data & old firmware
    Jaws 1.5X batts shipped before correct hex/GG files were ready
ECRT
  Checking batteries from customers for errors/bad data
  Checking number of cycles/SOH of batteries
Service (ZBAT)
  Battery programmer software used in c based Python library for ZBAT
    Handles battery validation and authentication
    Does data extraction: Part#, Cycles, SOH, etc. Saves $ on testing
    Corrupted EEPROM repair, saves $ on replacing batteries

## Slide 6
Zebra Confidential: For Internal Use Only
Going Forward
Additional battery support
  Zebra printer batteries
    Battery validation/authentication
    Displaying battery data
  BLE batteries
    Testing BLE beaconing functions
    Displaying BLE micro data
    Programming BLE micro
Add reading/writing of GG manufacturer blocks hex data
ZBAT Library updates
  Add GG update capability
  Add V2 PP+ battery support

## Slide 7
Zebra Confidential: For Internal Use Only
SharePoint Site
PDF Manual
TeraTerm serial terminal install program
Latest Zebra internal and JDM firmware
Release notes
Windows Battery Data Display program
  Display battery data from a hex file
  Only works with EEPROM/Auth data
Make bad hex file Windows program
  Creates errors in battery data for testing
  Only works with EEPROM/Auth data
https://zebra.sharepoint.com/sites/BatteryProgrammer

## Slide 8: Questions?