A short introduction to the
Battery Programming Box V2
Date: January 17, 2022

---
Overview
Overview
1. Device Overview
2. Basic Capabilities
3. Batteries Supported
4. Connections
5. Basic commands
6. Advanced commands
7. Firmware updates
8. SharePoint Site

---
What is it?
Device Overview
- Small device used to access and program battery ICs
- Reads/writes EEPROM, Auth IC, and Gas Gauges
- USB interface to PC
- Supports most Zebra terminal battery types
- Can support zebra printer batteries
- Status LED shows connection status and indicates when it’s accessing a battery

---
Basic Capabilities
- Import battery EEPROM/Auth IC file data onto your PC
- Display battery EEPROM/Auth IC data
  - Part number and revision, JEITA data, etc.
- Display gas gauge data
  - Cycle count, accumulated charge
  - Time since first use, status registers, etc.
- Update/replace EEPROM/Auth IC data
- Validate battery data to check for errors
- Authenticate the auth IC
- Display battery voltage and thermistor resistance

---
Batteries Supported
- MPA2 Smart Batteries (MC33 legacy)
- Pollux batts (TC70)
- PP+ Batts (TC70X, TC51, TC8000, MC18, etc.)
- Value tier (TC21, MC22, etc.)
- PP+ V2 (New GG) (Jaws, etc.)
- Hardware support for BLE battery
  - Simulate terminal power modes (on, off, suspended)
  - Simulate battery in & out of terminal
- Hardware can support Zebra printer 2 cell packs

---
Connections
- Micro USB cable to PC
  - Box appears as a USB serial port
    - Use a serial terminal program like TeraTerm
    - Simple command line interface
  - Also appears as a 2MB USB flash drive
    - Drag/drop files to/from the box
- Battery connections
  - Batt+, SCL, SDA, Gnd, and thermistor

---
Basic Commands
- ? – Context sensitive help menu
- B – Select battery type
- VBD – Validate battery data (Same process as terminal)
- DPP – Display Power Precision battery data
- DPP+ – Display Power Precision Plus battery data
- DGG – Display gas gauge data
- RE/RA – Read EEPROM/Auth IC into buffer
- WE/WA – Program EEPROM/Auth IC from buffer
- UE/UA – Update EEPROM/Auth IC from buffer
  - Does not erase data written during manufacture
- SF – Save buffer to a file on internal drive
- LF – Load buffer from a file on internal drive

---
Advanced Commands
- SGGF – Save gas gauge flash to a hex file
- HGG – Hibernate gas gauge
- RGG – Reset gas gauge
- USGG – Unseal gas gauge
- FUSGG – Fully unseal gas gauge
- DGGH – Display gas gauge registers in hex
- UGG – Update gas gauge
- Plan is to support BLE battery going forward
  - Read BLE micro firmware version, etc.
  - Trigger BLE beacon for testing

---
Firmware Updates
- Latest firmware is on SharePoint site
- UF ‘Update Firmware’ command triggers update
- Device will restart and connect to USB as a flash drive
- Drag and drop the new firmware file onto the drive
- Device will restart with updated code

---
SharePoint Site
https://zebra.sharepoint.com/sites/BatteryProgrammer
- Manual in PDF
- TeraTerm install program
- Windows Battery Data Display program
  - Display battery data from a hex file
  - Only works with EEPROM/Auth data
- Latest firmware and release notes

---
Questions?